## Slide 1: Anomaly Detection via Topological feature Map (ADTM)
Maia Rosengarten
MapBox
Dr. Sowmya Ramachandran
Christian Belardi
Stottler Henke Associates, Inc.

## Slide 2: Outline
Objectives
Overview of the technical approach
Experimental validation
Future work

## Slide 3: ADTM Objectives
Develop a tool to aid astronauts on deep space exploration habitats on with fault detection and handling
  Develop and evaluate a human-in-the-loop decision-support system that uses machine learning approaches to achieve
    Automated anomaly detection and diagnosis
    Automated predictive health analysis
  Provide intelligent decision-support to detect faults and degradations, trace root causes, and perform mitigations

## Slide 4: ADTM Overview
Combined AI approach
  Unsupervised learning algorithm for anomalous subsystem behavior detection and prognostics
    Leverage Self-Organizing Maps
  Case-Based Reasoning for diagnosis and fault handling
Modular in nature, can supplement other NASA IHMS technologies

## Slide 5: Background: Self-Organizing Maps
2-layer Artificial Neural Network (also called Kohonen Map) that produces a low-dimensional representation of training samples
The output is a 2D map of “Neurons,” each representing a cluster of input data
Unlike kMeans, the 2D output preserves topology of input (e.g. points close together in n-Dimensional space are close together in 2-D space) - useful for visualizing data

## Slide 6: SOM: An Elaboration
Associate each neuron with n-dimensional weight vector
For each n-dimensional input x:
  Compare x with weight vectors. Closest is “Best Matching Unit” (BMU)
  Move BMU and its “neighbors” in direction of input (topology preserving)
Dimensionality Reduction of n-D input to 2D map
“Self-organizing” weight updates

## Slide 7: SOM for Anomaly Detection
Train one or more SOMs on nominal subsystem behavior
Each cluster could represent an operational state
New points are classified as anomalous if they deviate from nominal clusters beyond tuned threshold
  The distance between the input data and each neuron weight is computed
  The best matching unit (BMU) is the one with the lowest distance
  MQE=distance between a data point and its BMU
  Data items falling outside the defined range of acceptable MQE are marked as anomalies
  The range of acceptable range defined based on the MQEs for the training data

## Slide 8: Anomaly Localization
Identify anomalous data points using algorithm described above
Create labeled data set
  Nominal data points with associated label “Nominal”
  Anomalous data points with associated label “Anomalous”
  Use supervised classification algorithms to extract high-information features to localize the anomaly to a subset of sensors

## Slide 9: From Detection to Diagnosis
Unsupervised learning can address detection
Diagnosis requires supervised learning and/or model-based analysis
We propose Case-Based Reasoning (CBR) for diagnosis and remediation
  CBR models can evolve incrementally over time
  CBR is intuitive because it is designed to mimic human analogical reasoning
Possible risk: CBR requires human-in-the-loop
  Mitigation: Models may be built on Earth before the launch of the mission
  Mitigation: We will explore the option of using localized model-based inference to support diagnosis

## Slide 10: Background: Case-Based Reasoning
AI technique for problem-solving by analogy
CBR consists of the following basic four steps:
  RETRIEVE the most similar cases 🖥
  REUSE the information and knowledge in the retrieved case(s) to solve the problem. 🖥 👤
  REVISE the solution used in the retrieved case(s). 🖥
  RETAIN this experience for future problem solving. 🖥
FOR ADTM, a case represents one known operating condition (nominal/fault)
  Previously encountered and modeled
    During system development, or
    Prior incident
  Case-base updated with each new condition encountered

## Slide 11: Humans as Sensors
Anomalies in human sensor data can serve as early indicators of problems in the environment
  E.g. Patterns of anomalies in HRV can be indicative of outgassing events or insufficient CO2 removals from the habitat
  Environment has a significant impact on human health and physiology
  Biosensors can help track human health over time and detect deviations from the normal
For more information on this, please refer to Dr. Wolfgang Fink’s presentation/paper in this conference

## Slide 12: Validation of anomaly detection approach
Validated the performance of ADTM’s anomaly detection and localization capabilities on a CubeSat (named “LabSat”)
Three connected boards (subsystems)
Induced various faults using a LabSat simulator
  Faults in each subsystems
  Mixture of faults local to a subsystem and those spanning more than one board

## Slide 13: LABSAT System: System Overview

## Slide 14: LABSAT: States modeled
Test Set | Description | Boards Affected
Solar Array 1, 1 Cell Shorted | Solar Array 1 has one photovoltaic cell shorted, reducing voltage from ~13.1 V (nominal) to ~11 V. | Board 1. Any Board 2 components connected to Solar Array 1 are affected by reduced power.
CDH Voltage Sensor Drifts High | Voltage sensor outgoing the CDH Load monotonically drifts high from sensor degradation over time. This is not a fault in the CDH Load itself, but rather with its voltage sensor. | Board 2
5V Regulator 1 - Failed | There is a redundant pair of 5V Regulators on Board 3. In this test case, the first “5V Regulator 1” has faulted. | Board 3
Nominal | Data of nominal operation was collected for each board and held out from the training set. | N/A

## Slide 15: LabSat: Data overview
Subsystem | # Rows | # Measurands
Board 1 | 2304 | 20
Board 2 | 1154 | 20
Board 3 | 2022 | 22
Training Data Size

## Slide 16: Phase I Results Summary
ADTM successfully identified previously unseen anomalies in all data sets
Sometimes the novel behaviors are not necessarily faults
ADTM was also effective in localizing the anomalies to pertinent sensors
  However, the localized features are not always the “cause” of the anomaly

## Slide 17: LABSAT: Anomalies detected
Test Cases | BOARD1-SOM | BOARD2-SOM | BOARD3-SOM
SA1-SHORT1 | 99.5% | 98% | 4%
CDH-VDRIFT | 0% | 100% | 3%
5VREG-FAIL | 3% | 0% | 100%
NOMINAL | 1% | 1% | 0%

## Slide 18: LABSAT: ANOMALY LOCALIZATION Results
SOM | Salient Feature
BOARD1-SOM | PPT1 V SA1 V Switch Battery1 to PPT2
BOARD2-SOM | UNREG COMM V CDH Amps UNREG COMM on Bus2 REG COMM on Bus2
SA1-SHORT1

## Slide 19: Conclusion and Future Work
The anomaly detection and localization approach is effective
  Encouraging results have been obtained on data from other systems
Future plans
Implement and validate CBR approach to diagnosis
Hierarchical modeling
Fusing data arriving at different resolutions
Implementing prognostic health predictions using SOMs
Develop a user-facing application for space habitats that incorporates these analytics